## Slide 1: STM32
Micro102

## Slide 2: CONTENT
GPIO lab
EXTI lab
SLEEP lab
STOP lab
STANDBY lab
DMA Pool lab
DMA Interrupt lab
RTC Alarm lab

## Slide 3: GPIO Lab 1

## Slide 4: Configure GPIO for LED toggling
Objective
  Learn how to setup pin and GPIO port in Cube MX
  How to generate project in Cube MX and use HAL functions
Goal
  Configure GPIO pin in Cube MX and generate project
  Add in to project HAL_Delay function and HAL_GPIO_Toggle function
  Verify the correct functionality on toggling LED
1

## Slide 5: Configure GPIO for LED toggling
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Configure LED pin as GPIO_Output
1

## Slide 6: Configure GPIO for LED toggling
Clock Configuration
  TAB->Clock Configuration
1
We can easily setup STM32 clocks

## Slide 7: Configure GPIO for LED toggling
The clock Configuration thee is interactive version of tree from RM
1
RM0090 Chapter 6 Reset and clock control Page 151

## Slide 8: Configure GPIO for LED toggling
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can generate project
  Menu > Project > Generate Project
1

## Slide 9: Configure GPIO for LED toggling
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinite loop while(1){ }
For toggling we need to use this functions
  HAL_HAL_Delay which create specific delay
  HAL_GPIO_WritePin or HAL_GPIO_TogglePin
1

## Slide 10: Configure GPIO for LED toggling
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
  Into infinit loop while(1){ }
For toggling we need to use this functions
  HAL_HAL_Delay which create specific delay
  HAL_GPIO_WritePin or HAL_GPIO_TogglePin
1
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_GPIO_WritePin(GPIOG, GPIO_PIN_13, GPIO_PIN_SET);
HAL_Delay(500);
HAL_GPIO_WritePin(GPIOG, GPIO_PIN_13, GPIO_PIN_RESET);
HAL_Delay(500);
}
/* USER CODE END 3 */

## Slide 11: EXTI lab 2

## Slide 12: Configure EXTI which turns on LED
Objective
  Learn how to setup input pin with EXTI in Cube MX
  How to generate project in Cube MX and use HAL functions
Goal
  Configure GPIO and EXTI pin in Cube MX and generate project
  Add into project Callback function and function which turn on led
  Verify the correct functionality by pressing button which turns on LED
2

## Slide 13: Configure EXTI which turns on LED
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Configure LED pin as GPIO_Output
Configure Button pin as GPIO_EXTIX
2

## Slide 14: Configure EXTI which turns on LED
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Configure LED pin as GPIO_Output
Configure Button pin as GPIO_EXTIX
2

## Slide 15: Configure EXTI which turns on LED
In order to make HAL_Delay to work correctly we need to setup clock system
Details in lab 0
2

## Slide 16: Configure EXTI which turns on LED
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can generate project
  Menu > Project > Generate Project
2

## Slide 17: Configure EXTI which turns on LED
HAL Library work flow 1
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
Generated by CubeMX

## Slide 18: Configure EXTI which turns on LED
HAL Library work flow 2
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
MX_GPIO_Init
inside main.c

## Slide 19: Configure EXTI which turns on LED
HAL Library working flow 3
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
inside stm32f4xx_it.c

## Slide 20: Configure EXTI which turns on LED
HAL Library work flow 4
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
User must define Callback it is declared by default as empty weak

## Slide 21: Configure EXTI which turns on LED
HAL Library work flow 5
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
Usually in main.c between /* USER CODE BEGIN */
tags

## Slide 22: Configure EXTI which turns on LED
HAL Library work flow summary
2
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
2. init GPIO
1. init NVIC
3. create edge
4. EXTI interrupt handler
5. HAL EXTI interrupt handler
6. HAL EXTI callback
HAL files clearing flags, check errors, …

## Slide 23: Configure EXTI which turns on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on we need to use this functions
  HAL_GPIO_WritePin
2

## Slide 24: Configure EXTI which turns on LED
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
  We create function which will handle the EXTI interrupts
The HAL callback function for EXTI
  void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
For LED turn on we need to use this functions
  HAL_GPIO_WritePin
2
/* USER CODE BEGIN 4 */
void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)
{
if(GPIO_Pin == GPIO_PIN_0) {
HAL_GPIO_WritePin(GPIOG, GPIO_PIN_14, GPIO_PIN_SET);
} else {
__NOP();
}
}
/* USER CODE END 4 */

## Slide 25: Low Power mode SLEEP lab 3

## Slide 26: Use SLEEP mode with EXTI
Objective
  We use the EXTI setup from lab 1
  Learn how to setup SLEEP in HAL
  Create simple project with SLEEP mode with wake up on pin press
Goal
  Use project from EXTI lab
  Learn how to setup the SLEEP in HAL, which events can wake up you
  Verify the correct functionality by measuring consumption
3

## Slide 27: SLEEP Mode
DMA
Core
CM4
Power regulator
RAM
Clock
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
Core is stopped
Peripherals are running
HSE
HSI
LSE
LSI
FLASH

## Slide 28: Use SLEEP mode with EXTI
HAL Library work flow summary
3
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
2. init GPIO
1. init NVIC
4. create edge
6. HAL EXTI interrupt handler
7. HAL EXTI callback
HAL files clearing flags, check errors, …
Enter into SLEEP mode(WFI)
3. Use WFI
5. EXTI interrupt handler

## Slide 29: Use SLEEP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSLEEPMode(uint32_t Regulator, uint8_t SLEEPEntry)
  We can measure consumption
3
To be able reprogram the STM32 which is in LP mode we must use connection under reset option

## Slide 30: Use SLEEP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSLEEPMode(uint32_t Regulator, uint8_t SLEEPEntry)
  We can measure consumption
3

## Slide 31: Use SLEEP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSLEEPMode(uint32_t Regulator, uint8_t SLEEPEntry)
  We can measure consumption
3
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_Delay(1000);
HAL_PWR_EnterSLEEPMode(PWR_LOWPOWERREGULATOR_ON,PWR_SLEEPENTRY_WFI);
}
/* USER CODE END 3 */

## Slide 32: Use SLEEP mode with EXTI
Consumption still to high?
  Is STM32 really in SLEEP?
  Is the Systick disabled?
  Is this better?
3
Notes: In run approx. 53mA
Consumption on STM32F429disco approx. 24.2mA in sleep
You ma test the difference with pins ins floating in and analog

## Slide 33: Use SLEEP mode with EXTI
Consumption still to high?
  Is STM32 really in SLEEP?
  Is the Systick disabled?
  Is this better?
3
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_Delay(1000);
HAL_SuspendTick();
HAL_PWR_EnterSLEEPMode(PWR_LOWPOWERREGULATOR_ON,PWR_SLEEPENTRY_WFI);
HAL_ResumeTick();
}
/* USER CODE END 3 */
Notes: In run approx. 53mA
Consumption on STM32F429disco approx. 24.2mA in sleep
You ma test the difference with pins ins floating in and analog

## Slide 34: Low Power mode STOP lab 4

## Slide 35: Use STOP mode with EXTI
Objective
  We use the EXTI setup from lab 1
  Learn how to setup STOP in HAL
  Create simple project with STOP mode with wake up on pin press
Goal
  Use project from EXTI lab
  Learn how to setup the STOP in HAL, which events can wake up you
  Verify the correct functionality by measuring consumption
4

## Slide 36: STOP Mode
Clock
DMA
Core
CM4
Power regulator
FLASH
RAM
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
HSE
HSI
LSE
LSI
Core is stopped
HSE, MSI clocks are OFF
SRAM and registers content is preserved
Peripherals with HSI, LSI, LSE clock option can be ON
GPIO’s keep their setup
Notes: The Stop mode is based on the Cortex™-M0+ deepsleep mode combined with peripheral clock gating.
HSI ON/OFF is optional

## Slide 37: Use STOP mode with EXTI
HAL Library work flow summary
4
Configure the GPIO to generate interrupt on rising or falling edge
Peripheral Initializations
including peripheral interrupt NVIC initializations
HAL_EXTI0_IRQHandler
Edge detection callback
HAL_GPIO_EXTI_Callback
EXTI0_IRQHandler
2. init GPIO
1. init NVIC
4. create edge
6. HAL EXTI interrupt handler
7. HAL EXTI callback
HAL files clearing flags, check errors, …
Enter into STOP mode(WFI)
3. Use WFI
5. EXTI interrupt handler
Clock reconfigure
8. Reconfigure clock after wakeup

## Slide 38: Use STOP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  HAL_PWREx_EnterUnderDriveSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  We can measure consumption
4
To be able reprogram the STM32 which is in LP mode we must use connection under reset option

## Slide 39: Use STOP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  HAL_PWREx_EnterUnderDriveSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  We can measure consumption
4

## Slide 40: Use STOP mode with EXTI
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  HAL_PWREx_EnterUnderDriveSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  We can measure consumption
4
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_Delay(1000);
HAL_PWR_EnterSTOPMode(PWR_LOWPOWERREGULATOR_ON,PWR_STOPENTRY_WFI);
SystemClock_Config();
}
/* USER CODE END 3 */

## Slide 41: Use STOP mode with EXTI
Or different function
4
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_Delay(1000);
HAL_PWREx_EnterUnderDriveSTOPMode(PWR_LOWPOWERREGULATOR_UNDERDRIVE_ON,PWR_STOPENTRY_WFI);
SystemClock_Config();
}
/* USER CODE END 3 */
Notes: In run approx. 53mA
Consumption on STM32F429disco approx. 5mA in stop(not optimized)
You ma test the difference with pins ins floating in and analog

## Slide 42: Low Power mode STANDBY lab 5

## Slide 43: Use STANDBY mode
Objective
  Learn how to setup STANDBY in HAL
  Create simple project with STANDBY mode with wake up on pin press
Goal
  Use project from EXTI lab
  Learn how to setup the STANDBY in HAL, which events can wake up you
  Verify the correct functionality by measuring consumption
5

## Slide 44: STANDBY Mode
Clock
DMA
Core
CM4
Power regulator
FLASH
RAM
USART
GP timers
DAC
USB
SPI
ADC
I2C
GPIO’s
RTC/backup reg.
IWDG
Reset
HSE
HSI
LSE
LSI
Core and all peripherals are OFF, except RTC and IWDG if enabled
HSE, MSI, HSI clocks are OFF, LSI LSE can be ON
SRAM and registers content is lost, except RTC, and standby circuitry
GPIO’s are in high Z, except Reset, RTC OUT and WKUP 1,2,3
Reset
RTC OUT
WKUP 1,2,3
Notes: The Standby mode allows to achieve the lowest power consumption. It is based on the
Cortex™-M0+ deepsleep mode, with the voltage regulator disabled. The VCORE domain is
consequently powered off. The PLL, the MSI, the HSI16 oscillator and the HSE oscillator
are also switched off. SRAM and register contents are lost except for the RTC registers,
RTC backup registers and Standby circuitry

## Slide 45: Use STANDBY mode
HAL Library work flow summary
5
Enable Wake-up pin
Peripheral Initializations
including peripheral interrupt NVIC initializations
2. Standby
1. init NVIC
4. create edge
Enter into STANDBY mode(WFI)
3. Use WFI
Reset
5. Wake up STM with reset

## Slide 46: Use STANDBY mode
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter STANDBY
  HAL_PWR_EnableWakeUpPin(uint32_t WakeUpPinx)
  HAL_PWR_EnterSTANDBYMode();
  We can measure consumption
5
To be able reprogram the STM32 which is in LP mode we must use connection under reset option

## Slide 47: Use STANDBY mode
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
Function to enter SLEEP
  HAL_PWR_EnterSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  HAL_PWREx_EnterUnderDriveSTOPMode(uint32_t Regulator, uint8_t STOPEntry)
  We can measure consumption
5
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_GPIO_TogglePin(GPIOG, GPIO_PIN_14);
HAL_Delay(2000);
HAL_PWR_EnableWakeUpPin(PWR_WAKEUP_PIN1);
HAL_PWR_EnterSTANDBYMode();
}
/* USER CODE END 3 */

## Slide 48: Use STANDBY mode
We cannot go into STANDBY again?
Try to clear wake up flag
  __HAL_PWR_CLEAR_FLAG(PWR_FLAG_WU);
5
/* USER CODE BEGIN 2 */
__HAL_PWR_CLEAR_FLAG(PWR_FLAG_WU);
/* USER CODE END 2 */

## Slide 49: Data transfer over DMA lab 6

## Slide 50: Use DMA in M2M transfer
Objective
  Learn how to setup DMA transfer in CubeMX
  Create simple DMA memory to memory transfer from RAM to RAM
Goal
  Use CubeMX and generate project with DMA
  Learn how to setup the DMA in HAL
  Verify the correct functionality by comparing transferred buffers
6

## Slide 51: Use DMA in M2M transfer
6
SRAM1
112KB
SRAM2
16KB
FSMC
AHB2
Multi-AHB Bus Matrix
ART
Accelerator
CORTEX-M4
168MHz
w/ FPU & MPU
Master 1
D-Bus
S-Bus
I-Code
D-Code
Dual Port
DMA2
Master 3
FIFO/8 Streams
AHB1
Dual Port
AHB1-APB1
Dual Port
AHB1-APB2
FLASH
1Mbytes
Dual Port
DMA1
Master 2
FIFO/8 Streams
CCM data RAM
64KB
High Speed
USB2.0
Master 4
FIFO/DMA
Ethernet
10/100
Master 5
FIFO/DMA
I-Bus

## Slide 52: Use DMA in M2M transfer
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
For DMA we don’t need to configure any pins
6

## Slide 53: Use DMA in M2M transfer
In order to make HAL_Delay to work correctly we need to setup clock system
Details in lab 0
6

## Slide 54: Use DMA in M2M transfer
6
DMA configuration
  TAB->Configuration
  System->DMA
  TAB->DMA2
  Button ADD
1. TAB -> Configuration
2. System DMA
3. TAB->DMA 2
4. Add DMA channel

## Slide 55: Use DMA in M2M transfer
6
DMA configuration
  Select MEMTOMEM DMA request
  Normal mode
  Increment source and destination address
  FIFO setup
  Byte data width
  Burst size
  Button OK
1. MEMTOMEM
2. Normal mode
3. Increment addresses
4. FIFO setup
5. Data width and Burst
6. OK

## Slide 56: Use DMA in M2M transfer
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can generate project
  Menu > Project > Generate Project
6

## Slide 57: Use DMA in M2M transfer
Start process DMA (same for TIM, ADC)
  Non blocking start process
  The end of the process must be checked by pooling
6
Peripheral Initializations
Start Process
(HAL_DMA_Start)
Poll for process complete
(PollForTransfer)
1. init DMA
2. Start DMA
3. DMA transfer data
4. Check if transfer is complete

## Slide 58: Use DMA in M2M transfer
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
HAL functions for DMA
  HAL_DMA_Start(DMA_HandleTypeDef *hdma, uint32_t SrcAddress, uint32_t DstAddress, uint32_t DataLength)
  HAL_DMA_PollForTransfer(DMA_HandleTypeDef *hdma, uint32_t CompleteLevel, uint32_t Timeout)
6

## Slide 59: Use DMA in M2M transfer
We create tow buffers
  One with source data
  Second as destination buffer
6
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
/* USER CODE END 0 */

## Slide 60: Use DMA in M2M transfer
HAL_DMA_Start start the M2M data transfer
HAL_DMA_PollForTransfer check if the transfer ends successfuly
6
/* USER CODE BEGIN 2 */
HAL_DMA_Start(&hdma_memtomem_dma2_stream0, (uint32_t) (Buffer_Src), (uint32_t) (Buffer_Dest), 10);
while(HAL_DMA_PollForTransfer(&hdma_memtomem_dma2_stream0, HAL_DMA_FULL_TRANSFER, 100) != HAL_OK)
{
__NOP();
}
/* USER CODE END 2 */

## Slide 61: Data transfer over DMA with interrupt lab 7

## Slide 62: Use DMA M2M transfer with interrupt
Objective
  Learn how to setup DMA transfer with interrupt in CubeMX
  Create simple DMA memory to memory transfer from RAM to RAM
Goal
  Use CubeMX and generate project with DMA
  Learn how to setup the DMA in HAL
  Verify the correct functionality by comparing transferred buffers
7

## Slide 63: Use DMA M2M transfer with interrupt
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
For DMA we don’t need to configure any pins
7

## Slide 64: Use DMA M2M transfer with interrupt
In order to make HAL_Delay to work correctly we need to setup clock system
Details in lab 0
7

## Slide 65: Use DMA M2M transfer with interrupt
7
DMA configuration
  TAB->Configuration
  System->DMA
  TAB->DMA2
  Button ADD
1. TAB -> Configuration
2. System DMA
3. TAB->DMA 2
4. Add DMA channel

## Slide 66: Use DMA M2M transfer with interrupt
7
DMA configuration
  Select MEMTOMEM DMA request
  Normal mode
  Increment source and destination address
  FIFO setup
  Byte data width
  Burst size
  Button OK
1. MEMTOMEM
2. Normal mode
3. Increment addresses
4. FIFO setup
5. Data width and Burst
6. OK

## Slide 67: Use DMA M2M transfer with interrupt
7
DMA configuration
  System -> NVIC
  Enable DMA2 Stream interrupt
  Button OK
1. TAB -> Configuration
3. Enable DMA2 interrupts
2. System -> NVIC
4. OK

## Slide 68: Use DMA M2M transfer with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can generate project
  Menu > Project > Generate Project
7

## Slide 69: Use DMA M2M transfer with interrupt
HAL Library DMA with IT flow
7
Start process with interrupt generation at end of process
HAL_DMA_Start_IT
DMA Initializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
end of process callback
DMA_XferCpltCallback
process Error callback
DMA_XferErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
DMA2_Stream0_IRQHandler
1. DMA init
2. DMA transfer start
3. DMA transfer complete or error
4. HAL DMA management
5. DMA transfer was correct
5. Error in DMA transfer

## Slide 70: Use DMA M2M transfer with interrupt
Now we open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
DMA callback function
  We need to add the name of callback function into DMA structure
HAL functions for DMA
  HAL_DMA_Start_IT(DMA_HandleTypeDef *hdma, uint32_t SrcAddress, uint32_t DstAddress, uint32_t DataLength)
7

## Slide 71: Use DMA M2M transfer with interrupt
We create tow buffers
  One with source data
  Second as destination buffer
7
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
/* USER CODE END 0 */

## Slide 72: Use DMA M2M transfer with interrupt
DMA callback creation function prototype
DMA complete callback with nop where we can put breakpoint
7
/* USER CODE BEGIN 4 */
void XferCpltCallback(DMA_HandleTypeDef *hdma)
{
__NOP();//we reach this only if DMA transfer was correct
}
/* USER CODE END 4 */
/* USER CODE BEGIN 0 */
uint8_t Buffer_Src[]={0,1,2,3,4,5,6,7,8,9};
uint8_t Buffer_Dest[10];
void XferCpltCallback(DMA_HandleTypeDef *hdma);
/* USER CODE END 0 */

## Slide 73: Use DMA M2M transfer with interrupt
DMA Start
  Before we start the DMA with interrupt we need to set the callback into DMA structure
  Then is possible use the HAL_DMA_Start_IT to begin DMA transfer
7
/* USER CODE BEGIN 2 */
hdma_memtomem_dma2_stream0.XferCpltCallback=&XferCpltCallback;
HAL_DMA_Start_IT(&hdma_memtomem_dma2_stream0,(uint32_t)Buffer_Src,(uint32_t)Buffer_Dest,10);
/* USER CODE END 2 */

## Slide 74: Use RTC Alarm lab 8

## Slide 75: Use RTC and Alarm with interrupt
Objective
  Learn how to setup RTC with interrupt in CubeMX
  Create simple RTC project with periodic alarm interrupt
Goal
  Use CubeMX and generate project with RTC
  Learn how to setup the RTC in HAL
  Verify the correct functionality by periodic RTC alarm interrupts
8

## Slide 76: Use RTC and Alarm with interrupt
Create project in Cube MX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
Set Internal Alarm on Alarm A or Alarm B
Set GPIO to toggle with LED as alarm indication
8

## Slide 77: Use RTC and Alarm with interrupt
In order to make HAL_Delay to work correctly we need to setup clock system
Details in the next slide
8

## Slide 78: Use RTC and Alarm with interrupt
Clock Configuration overview 26
RTC
  TAB>Pinout
  RCC>RTC set RTC feature
  TAB>Clock Configuration
  Now the RTC can be set
1. RTC disabled
2. RTC set
3. Set RTC
8

## Slide 79: Use RTC and Alarm with interrupt
RTC Configuration
  TAB->Configuration
  Control -> RTC
  Set parameters which you want
8
1. TAB -> Configuration
2. RTC
3. Check configuration

## Slide 80: Use RTC and Alarm with interrupt
RTC Configuration NVIC
  TAB->NVIC Setup
  Enable Alarm interrupt
  Button OK
8
1. TAB -> NVIC
2. Enable RTC Alarm
3. Button OK

## Slide 81: Use RTC and Alarm with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can generate project
  Menu > Project > Generate Project
8

## Slide 82: Use RTC and Alarm with interrupt
The RTC can be preserved during RESET(ok LP modes)
  CubeMX not enable the RTC by default
  We need to add HAL_PWR_EnableBkUpAccess() and __HAL_RCC_RTC_ENABLE() before we call MX_RTC_Init()
Set the first alarm to 1s
  In MX_RTC_Init
We create the RTC interrupt handler and we reconfigure the Alarm A time
  HAL_RTC_AlarmAEventCallback(RTC_HandleTypeDef *hrtc)
  HAL_RTC_GetAlarm(RTC_HandleTypeDef *hrtc, RTC_AlarmTypeDef *sAlarm, uint32_t Alarm, uint32_t Format)
  HAL_RTC_SetAlarm_IT(RTC_HandleTypeDef *hrtc, RTC_AlarmTypeDef *sAlarm, uint32_t Format)
RTC alarm indication will be done by LED
  HAL_GPIO_TogglePin(GPIO_TypeDef* GPIOx, uint16_t GPIO_Pin)
8

## Slide 83: Use RTC and Alarm with interrupt
RTC enable
In MX_RTC_Init we set first Alarm to 1s
8
/* Initialize all configured peripherals */
HAL_PWR_EnableBkUpAccess();//enable PWR backup domain access (RTC,BKReg)
__HAL_RCC_RTC_ENABLE();//Enable RTC. not created by cube because the RTC can run.
MX_GPIO_Init();
MX_RTC_Init();
/**Enable the Alarm A
*/
sAlarm.AlarmTime.Hours = 0;
sAlarm.AlarmTime.Minutes = 0;
sAlarm.AlarmTime.Seconds = 1;
sAlarm.AlarmTime.SubSeconds = 0;

## Slide 84: Use RTC and Alarm with interrupt
RTC enable
8
/* USER CODE BEGIN 4 */
void HAL_RTC_AlarmAEventCallback(RTC_HandleTypeDef *hrtc){
RTC_AlarmTypeDef sAlarm;
HAL_RTC_GetAlarm(hrtc,&sAlarm,RTC_ALARM_A,FORMAT_BIN);
if(sAlarm.AlarmTime.Seconds>58){
sAlarm.AlarmTime.Seconds=0;
}else{
sAlarm.AlarmTime.Seconds=sAlarm.AlarmTime.Seconds+1;
}
while(HAL_RTC_SetAlarm_IT(hrtc, &sAlarm, FORMAT_BIN)!=HAL_OK){}
HAL_GPIO_TogglePin(GPIOG,GPIO_PIN_14);
}
/* USER CODE END 4 */

## Slide 85: Use RTC and Alarm with interrupt
Advanced task
  The counting stops after 1minute
  Modify the project to create alarm every 1s for infinite time
We only need to modify the Alarm mask to ignore Days, Hours and Minutes
8
/**Enable the Alarm A
*/
sAlarm.AlarmTime.Hours = 0;
sAlarm.AlarmTime.Minutes = 0;
sAlarm.AlarmTime.Seconds = 1;
sAlarm.AlarmTime.SubSeconds = 0;
sAlarm.AlarmTime.TimeFormat = RTC_HOURFORMAT12_AM;
sAlarm.AlarmTime.DayLightSaving = RTC_DAYLIGHTSAVING_NONE;
sAlarm.AlarmTime.StoreOperation = RTC_STOREOPERATION_RESET;
sAlarm.AlarmMask = RTC_ALARMMASK_DATEWEEKDAY|RTC_ALARMMASK_HOURS|RTC_ALARMMASK_MINUTES;
sAlarm.AlarmSubSecondMask = RTC_ALARMSUBSECONDMASK_ALL;
sAlarm.AlarmDateWeekDaySel = RTC_ALARMDATEWEEKDAYSEL_DATE;
sAlarm.AlarmDateWeekDay = 1;
sAlarm.Alarm = RTC_ALARM_A;
HAL_RTC_SetAlarm_IT(&hrtc, &sAlarm, FORMAT_BCD);

## Slide 86: Thank You